## Slide 1: THOR-50M Modifications for Reclined Seating – Project Update and Preliminary Results NHTSA Contract No. DTNH2215D00022/693JJ919F000222
Jason Forman1, Justin McMahon1, Adrian Caudillo-Huerta1, Matthew Panzer1, William Marshall2, Derek Winter2
1University of Virginia Center for Applied Biomechanics
2Cellbond
July 5, 2020

## Slide 2
DISCLAIMER
This publication is distributed by the U.S. Department of Transportation, National Highway Traffic Safety Administration, in the interest of information exchange. The opinions, findings, and conclusions expressed in this publication are those of the authors and not necessarily those of the Department of Transportation or the National Highway Traffic Safety Administration. The United States Government assumes no liability for its contents or use thereof. If trade or manufacturers’ names are mentioned, it is only because they are considered essential to the object of the publication and should not be construed as an endorsement. The United States Government does not endorse products or manufacturers.
NOTE: This report is published in the interest of advancing motor vehicle safety research. While the report may provide results from research or tests using specifically identified motor vehicle models, it is not intended to make conclusions about the safety performance or safety compliance of those motor vehicles, and no such conclusions should be drawn.

## Slide 3: Positioning Study – Qualitative Analysis
2018 Honda Odyssey 2nd row captain’s chair
Honda Acura TLX Driver’s Chair
LAB seat with marionette positioning
Farside Buck which will hold TLX and Odyssey Seats
LAB Seat on HAV Gold Standard Buck
LAB Seat
Honda Acura TLX Driver’s Chair
Honda Odyssey 2nd row captain’s chair

## Slide 4: Positioning Study – Qualitative Analysis
Acura TLX Driver’s Chair
Honda Odyssey 2nd row captain’s chair
+ 3 intermediate angles,
slouched and erect,
pelvis moved forward
(more than 30 trials total)

## Slide 5: Positioning Study – Qualitative Analysis
LAB Seat
Zero Gravity Seat
Equiv. Seatback Angle 60°
Equiv. Seatback Angle 70°
Equiv. Seatback Angle 25°
Equiv. Seatback Angle 40°
Equiv. Seatback Angle 50°

## Slide 6: Major Observations
Jacket and Gaps
  Noticeable tension in the pelvis strap of the jacket
  Considerable gaps were observed between the pelvis flesh and the abdomen foam, the abdomen foam and ribcage, and the pelvis and thigh flesh
Pelvis Flesh
  Need to be able to keep thighs in contact with the seat, while allowing posterior pelvis rotation – pelvis flesh limits hip extension
  Saw interference between the posterior pelvis and thigh flesh
Lumbar Spine
  Separation of rubber and metal parts of the lumbar spine assembly in recline positions
  Significant moment seen in recline positions
  Need to allow placement into diversity of positions while still maintaining integrity

## Slide 7: Observations – Jacket

## Slide 8: Observations – Gaps

## Slide 9: Observations – Pelvis Flesh
Restricts ability to extend hips, keep contact between thigh and seat

## Slide 10: Observations – Lumbar Spine
Pulls apart under extension
In some cases, initial extension of the lumbar is natural consequence of the seat geometry (e.g., Odyssey)
To accommodate diverse seat designs, need to allow lumbar extension without pulling apart

## Slide 11: Preliminary Implementation of Design Concepts in NHTSA THOR FE Model: Upper Lumbar Flex Joint and Modified Pelvis/Thigh Flesh

## Slide 12: Upper Lumbar Flex Joint & Abdomen Plate
Base: publicly-available NHTSA THOR FE Model

## Slide 13: Pelvis & Thighs

## Slide 14: Pelvis Behavior
Experiments
Hex mesh
Tetra mesh
0° Pelvis
24° Pelvis
Anterior
Superior
Notes: Pelvis material models re-tuned to have similar behavior with both tetrahedral and hexahedral meshes.

## Slide 15: Pelvis Behavior
Experiments
Hex mesh
Tetra mesh
0° compression
24° compression
Anterior
Superior
Notes: Pelvis material models re-tuned to have similar behavior with both tetrahedral and hexahedral meshes.

## Slide 16: Simulation Assumptions
Natural gravity settling instead of attempting to match pelvis/T6 tilt sensor measurements (as in NHTSA THOR Qualifications and Procedures Manual).
As a result, some slight differences in initial position due to differences in settling
  Prefer this approach, as it reflects what should be expected in a real test
Propose to compare responses of stock THOR model to that of THOR with Cellbond’s modifications.
  Glimpse of overall trends of measurements of interest.
Simulations
  Certification Suite: upper & lower thorax impact, abdomen impact, & upper leg impact
  Gold Standard 1, 2, & 3
  Recline - LAB Seat
All simulations with Stock THOR have a neutral spine angle (closest to modified THOR)

## Slide 17: Upper Thorax Impact
Chart: ULFJ Angle
| 0 | 4.9995002746999999 | 9.9999008179000004 | 14.999401092999999 | 19.999801636000001 | 24.99930191 | 29.999700546 | 34.999202728 | 39.999603270999998 | 44.999103546000001 | 49.999504088999998 | 54.999900818 | 59.999401093000003 | 64.999801636000001 | 69.999305724999999 | 74.999702454000001 | 79.999206543 | 84.999603270999998 | 89.999107361 | 94.999504088999998 | 99.999908446999996 | 104.99940491 | 109.99980164 | 114.99930573 | 119.99970245 | 124.99920654 | 129.99960326999999 | 134.99909973000001 | 139.99951171999999 | 144.99990844999999 | 149.99940491000001 | 154.99980163999999 | 159.99931334999999 | 164.99971008 | 169.99920653999999 | 174.99960326999999 | 179.99911499000001 | 184.99951171999999 | 189.99990844999999 | 194.99940491000001 | 199.99981689000001 | 200.0007019
 | 3.453 | 3.4517 | 3.4982 | 3.5817 | 4.3238 | 5.6358 | 6.6069 | 7.8579 | 9.0838 | 10.1338 | 10.9074 | 11.4156 | 11.8248 | 11.6335 | 11.1045 | 10.3729 | 9.6254 | 9.0207 | 8.4843 | 8.2206 | 8.2601 | 8.384 | 8.4508 | 8.3999 | 8.3353 | 8.2176 | 8.0248 | 7.8175 | 7.5885 | 7.413 | 7.2691 | 7.204 | 7.162 | 7.0537 | 6.8938 | 6.7072 | 6.511 | 6.3869 | 6.2277 | 5.9837 | 5.6747 | 5.6747
Slight difference in initial positioning due to bending of the new upper lumbar flex joint during gravity settling. NHTSA corridors provided where applicable.
Stock THOR
Cellbond Modified
Chart: Impactor Force
corridor min | 2.449 | 2.449
corridor max | 2.855 | 2.855
Chart: Rib X-Displacement
corridor min | -46.4 | -46.4
corridor max | -38 | -38
Chart: Lumbar LC Y-Moment
A positive angle indicates forward flexion
Preliminary Results

## Slide 18: Lower Thorax Impact
Slight difference in initial positioning due to bending of the new upper lumbar flex joint during gravity settling. NHTSA corridors provided where applicable.
Stock THOR
Cellbond Modified
Chart: Impactor Force
corridor min | 3.058 | 3.058
corridor max | 3.68 | 3.68
Chart: Rib X-Displacement
corridor min | -55.3 | -55.3
corridor min | -45.4 | -45.4
Chart: Lumbar LC Y-Moment
Preliminary Results

## Slide 19: Lower Abdomen Impact
Slight difference in initial positioning due to bending of the new upper lumbar flex joint during gravity settling. NHTSA corridors provided where applicable.
Stock THOR
Cellbond Modified
Chart: Impactor Force
corridor min | 2.746 | 2.746
corridor max | 3.078 | 3.078
Chart: Abdomen IR-TRACC Displacement
corridor min | -70.1 | -70.1
corridor max | -92.9 | -92.9
Preliminary Results

## Slide 20: Upper Leg Impact
Stock THOR
Cellbond Modified
Chart: Impactor Force
corridor min | 4.278 | 4.278
corridor max | 5.093 | 5.093
Chart: Femur Force
corridor min | -2.712 | -2.712
corridor max | -3.314 | -3.314
Chart: Acetabulum Force
corridor min | 1.478 | 1.478
corridor max | 1.806 | 1.806
NHTSA corridors provided where applicable.
Preliminary Results

## Slide 21: Gold Standard 1
Stock THOR
Cellbond Modified
40 km/h, No Force Limiter
Preliminary Results

## Slide 22: Gold Standard 1 Cut View
Stock THOR
Cellbond Modified
40 km/h, No Force Limiter
Preliminary Results

## Slide 23: Gold Standard 1
Chart: GS1 Flex Joint Moments
Chart: Kinematic Plot
Chart: Kinematic Plot
Stock THOR
Cellbond Modified
Head
T1
Pelvis
Head
Chart: ULFJ Rotation
Left Shoulder
Right Shoulder
Negative Y is forward flexion.
Positive Z twists the spine to
turn rightward.
40 km/h, No Force Limiter
Preliminary Results

## Slide 24: Modified THOR in Gold Standard
GS1: lap belt slides into opening between pelvis and thighs due to slack from locking knees. Simulation will be re-run with modified jacket design when that is completed and then meshed and fit to THOR model.
GS1 w/o knee bolster: lap belt plays much greater role in restraining THOR and does not slide into opening.
Preliminary Results

## Slide 25: Gold Standard 2
Stock THOR
Cellbond Modified
30 km/h, 3 kN Force Limiter
Preliminary Results

## Slide 26: Gold Standard 2 Cut View
Stock THOR
Cellbond Modified
30 km/h, 3 kN Force Limiter
Preliminary Results

## Slide 27: Gold Standard 2
Chart: Kinematic Plot
Chart: Kinematic Plot
Stock THOR
Cellbond Modified
Head
T1
Pelvis
Head
Left Shoulder
Right Shoulder
Chart: ULFJ Rotation
Chart: GS2 Flex Joint Moments
Negative Y is forward flexion.
Positive Z twists the spine to
turn rightward.
30 km/h, 3 kN Force Limiter
Preliminary Results

## Slide 28: Gold Standard 3
Stock THOR
Cellbond Modified
30 km/h, 30° Oblique, 3 kN Force Limiter
Preliminary Results

## Slide 29: Gold Standard 3 Cut View
Stock THOR
Cellbond Modified
30 km/h, 30° Oblique, 3 kN Force Limiter
Preliminary Results

## Slide 30: Gold Standard 3
Chart: Kinematic Plot
Chart: Kinematic Plot
Stock THOR
Cellbond Modified
Head
T1
Pelvis
Head
Chart: ULFJ Rotation
Left Shoulder
Right Shoulder
Chart: GS3 Flex Joint Moments
Negative Y is forward flexion.
Positive Z twists the spine to
turn rightward.
30 km/h, 30° Oblique, 3 kN Force Limiter
Preliminary Results

## Slide 31: Reclined Simulations
Pulse Direction
Model for seat & restraints developed by Autoliv
LAB Seatpan – simplified with defined stiffness
Seatbelt has triple pretensioner, shoulder FL
50 km/h pulse (Uriot et al. 2015)
THOR positioning according to FARO points from Autoliv
  Pelvis reclined to angle of 48°
  H-point aligned with measurements
Feet rigidly constrained (like PMHS tests)
Matched PMHS tests performed previously at UVA (Richardson et al. 2019 ESV)
Preliminary Results

## Slide 32: Reclined
Stock THOR
Cellbond Modified
Preliminary Results

## Slide 33: Reclined Cut View
Stock THOR
Cellbond Modified
Preliminary Results

## Slide 34: Reclined
Chart: Kinematic Plot
Chart: Kinematic Plot
Chart: Flex Joint Moments
Stock THOR
Cellbond Modified
Head
T1
Pelvis
Head
Left Shoulder
Right Shoulder
Chart: ULFJ Rotation
Negative Y is forward flexion.
Positive Z twists the spine to
turn rightward.
Preliminary Results

## Slide 35: Pelvis Motion
Stock THOR
Cellbond Modified
Preliminary Results

## Slide 36: Pelvis Motion
Stock THOR
Cellbond Modified
Preliminary Results

## Slide 37: Lap Belt Forces
Preliminary Results

## Slide 38: Outboard Seatbelt Displacements
Stock THOR
Cellbond Modified
Lap Belt Δ = - L0
Preliminary Results

## Slide 39: Pelvis Observations
21.4 mm
0.81 mm
Preliminary Results

## Slide 40: Pelvis Sensitivity Study
Stock THOR
Cellbond Modified
Coxal Bone Mat. Replaced
Pelvis Stiffness x5
Pelvis Stiffness x10
Pelvis Stiffness x100
Cellbond Modified
Coxal Bone Material Replaced with Flesh Material
Preliminary Results

## Slide 41: Pelvis Sensitivity Study
Stock THOR
Cellbond Modified
Coxal Bone Mat. Replaced
Pelvis Stiffness x5
Pelvis Stiffness x10
Pelvis Stiffness x100
Cellbond Modified
Pelvis Stiffness x10
Preliminary Results

## Slide 42: Pelvis Sensitivity Study
Stock THOR
Cellbond Modified
Coxal Bone Mat. Replaced
Pelvis Stiffness x5
Pelvis Stiffness x10
Pelvis Stiffness x100
Cellbond Modified
Pelvis Stiffness x10
Preliminary Results

## Slide 43: Pelvis Sensitivity Study
Stock THOR
Cellbond Modified
Coxal Bone Mat. Replaced
Pelvis Stiffness x5
Pelvis Stiffness x10
Pelvis Stiffness x100
Coxal Bone Mat. Replace & Stiffness x10
Flipped Coxal Bone
Pelvis Stiffness x10
Flipped Coxal Bone
Preliminary Results

## Slide 44: Pelvis Sensitivity Study
Stock THOR
Cellbond Modified
Coxal Bone Mat. Replaced
Pelvis Stiffness x5
Pelvis Stiffness x10
Pelvis Stiffness x100
Coxal Bone Mat. Replace & Stiffness x10
Flipped Coxal Bone
Pelvis Stiffness x10
Flipped Coxal Bone
Preliminary Results

## Slide 45: Pelvis Sensitivity Study
Stock THOR
Cellbond Modified
Pelvis Stiffness x5
Pelvis Stiffness x10
Pelvis Stiffness x100
Preliminary Results

## Slide 46: Pelvis Sensitivity Study: Lumbar LC
Chart: Lumbar LC Y Moments
Chart: Lumbar LC Z Force
Chart: Lumbar LC Y Moments
Chart: Lumbar LC Z Force
Stock THOR
Cellbond Modified
Coxal Bone Mat. Replaced
Pelvis Stiffness x5
Pelvis Stiffness x10
Pelvis Stiffness x100
Preliminary Results

## Slide 47: THOR-50M Modifications for Reclined Seating – Project Update and Preliminary Results NHTSA Contract No. DTNH2215D00022/693JJ919F000222
Jason Forman1, Justin McMahon1, Adrian Caudillo-Huerta1, Matthew Panzer1, William Marshall2, Derek Winter2
1University of Virginia Center for Applied Biomechanics
2Cellbond
July 5, 2020